## Slide 1: Final Presentation I.L.A.T.S. (Infrared Light Asset Tracking System)
By:
Moheb Amini (mamin004@ucr.edu)
Mark Logston (mlogs001@ucr.edu)
Ahmed El Gabaly (aelga001@ucr.edu)

## Slide 2: Concept and Application of Design
A Real-Time Locating system (RTLS)
  Transmitters that send signals to receivers which determine object location
Uses Optical communication to transmit data
Related to Electronics, Optoelectronics, Signal Processing, Telecommunication and Embedded systems
This design is intended to be implemented in an industrial setting: mainly hospitals

## Slide 3: Technical Design Objective
Succeed to efficiently identify the location of the 2 different transmitters, each with it’s own unique signature, within 2 rooms and 1 hallway (3 receivers)
To Achieve this we need:
    Object motion in xyz values using accelerometer
    Transmit a signal of at least 8ft to receiver
    FFT of received signal to identify each signature
    Server response time of at least 400ms
    Have Low Power Consumption

## Slide 4
Final High Level Block Diagram Design
(For each room and object)
Changes from previous High Level Design:
- Incorporated a battery life checker on the objects
- Changed the type of IR Sensor in the room block
- Created another block in the diagram for online server
- Automatically access server through GUI
- Added FFT analysis to the room block

## Slide 5: Technical Challenges
Getting accurate data analysis using FFT
Amplification of the Photodiode signal
  Change photodiode to phototransistor
  Disregard TIA amplifier
Sending FFT data to an online server gathering and relaying data to GUI
Hardware Issues
  Sensor alignment
  Issue with MCU
  Sensor ADC value accuracy

## Slide 6: Major Tasks
Moheb Amini:
Communication from the Infrared LED and the Phototransistor
I2C communication from Accelerometer to a microcontroller
Creation of Circuits
Create FFT to analyze incoming signals
Transmitter PCB Design
3D printed Receiver Mount Design
Ahmed El Gabaly:
Set up the microcontroller of the photodiode to send the incoming data to Ethernet
Communication from the Photodiode microcontroller to the Server
Creation of Battery Life Checker
Receiver PCB Design
Mark Logston:
Creating the GUI
Creating the Database
Creation of Circuits
Alignment of Infrared Transistors
Helped in creation of Transmitter and Receiver PCBs

## Slide 7: Design considerations
Realistic constraints
  Power consumption of the Transmitter
  Cost of transmitter and Receiver
  Receiver mounting location
  Arduino Ram size
  Phototransistor vs. PhotoDiode
  Frequency choice
Industry Standards
  I2C
  TCP/IP
  IEEE 802.3 (Ethernet)
Changes:
  Mounting Location
  Using Phototransistor

## Slide 8: Test Report
To test the system as a whole we at first tested each part separately
  FFT of transmitted Signal to identify each transmitter
  Send data to online server and read data from server
  Distance from transmitter to receiver
    Able to get 8 ½ feet
  Server Response time
    Able to respond fast enough for normal walking speed
  GUI
  Power consumption: 0.506 𝜇W
Mounted Receivers above door and moved transmitters underneath seeing if the correct room/hallway number appeared on GUI in response to transmitter

## Slide 9: Demo
Video Demo:
http://youtu.be/8rx8W-GGqlw&hd=1

## Slide 10: Summary
Able to track two objects moving between two rooms and a hallway
  Infrared sensor reading Infrared waves at different frequencies
  FFT converting given input with multiple signals and noise
  Room Microcontroller send current object location via Ethernet
  Display Correct Room and Hallway Numbers on GUI by accessing the server